## Slide 1: Biodiesel for Research and Education
Research Presentation
Jennifer Keiner
Chris Behm

## Slide 2: Overview
Goals
Background
Procedures
Results & Conclusions
Future Research

## Slide 3: Goals
Determine the effect of parameters on the conversion of free fatty acids(FFA) of waste cooking oil(WCO)
Investigate effect of citric acid washings on water consumption for biodiesel purification processes
Analyze and compare biodiesel produced using methanol and ethanol

## Slide 4: Background
Biodiesel research started as an alternative fuel source to petroleum derived diesel, benefits include:
  A renewable energy resource
  Able to be blended with traditional diesel
  Less particulate matter, CO2 emissions, and sulfur dioxide emission

## Slide 5: Background Cont.
Potential Problems
    Production consumes a lot water, especially during feedstock development (growth of soybean)
Solutions
  Alternative feedstock that uses less water can be of great interest such as waste cooking oil
  Less water intensive techniques should be used for biodiesel purification methods (citric acid wash)

## Slide 7: Procedure
Acid Pre-treatment
  Materials:
    Waste cooking oil
    Methanol, 50:1 molar ratio
    H2SO4: (15% wt of FFA)
    Indicator solution
  Procedure:
    Prepare materials according to theoretical calculations
    Heat the oil to 56 C
    Add the sulfuric acid and methanol mixture
    Draw samples
    Titrate with NaOH to determine FFA

## Slide 8: Results & Conclusions
Chart: 
| 5 | 6 | 7 | 9 | 11 | 14 | 17 | 22 | 27 | 37 | 47 | 62 | 77 | 107 | 137 | 167 | 197
FFA Conversion 56C 15% FFA 5.557% | 0.025 | 0.025 | 0.125 | 0.025 | 0.025 | 0.1 | 0.1 | 0.175 | 0.1 | 0.25 | 0.25 | 0.275 | 0.3 | 0.375 | 0.425 | 0.5 | 0.575
FFA Conversion 56C 15% FFA 4.567% | 0.025641 | 0.057692 | 0.057692 | 0.26923 | 0.057692 | 0.19231 | 0.17308 | 0.23077 | 0.30769 | 0.31346 | 0.35256 | 0.42308 | 0.42308 | 0.44231 | 0.53846 | 0.50641 | 0.64103 | 0.57051 | 0.57051 | 0.57051 | 0.57051 | 0.60897 | 0.64744
FFA Conversion 58C 10% FFA 4.756% | 0.025027 | 0.075026 | 0.050026 | 0.075026 | 0.10003 | 0.12502 | 0.17502 | 0.15002 | 0.17502 | 0.20002 | 0.25002 | 0.30002 | 0.37502 | 0.40002 | 0.42502 | 0.47501
FFA Conversion 56C 15% FFA 5.026% (50:1) | 0.16535 | 0.22047 | 0.40945 | 0.40945 | 0.50394 | 0.46457 | 0.58268 | 0.6378 | 0.64567 | 0.71654 | 0.77165 | 0.7874 | 0.83465 | 0.81102 | 0.81102 | 0.81102 | 0.85827 | 0.85827 | 0.90551 | 0.90551 | 0.90551 | 0.90551
Time (Minutes)
FFA
Conversion
Conversion of FFA Graph

## Slide 9: Procedure
Citric Acid Wash
  Materials:
    Crude biodiesel
    1:1 ratio of wash of water, 2%, 3%, and 4% citric acid solution to biodiesel
  Procedure:
    Separate crude biodiesel into 4 separation funnels.
    Add the four types of washes to each funnel.
    Let sit for 30 minutes.
    Drain the washing solution.
    Take a 3 mL sample of the biodiesel.
    Repeat until water comes clear..
    In a test tube mix, biodiesel sample, methanol and shake for 10 seconds.
    Impurities will settle to the bottom allowing identification of the best washing solution.

## Slide 10: Results & Conclusions
Left picture: Waste water from biodiesel washing.
Left was only water and was cloudy after the 2nd wash.
Water was not as effective as citric acid solution after the first and second wash.
Concentration of citric acid had a minimal effect.

## Slide 11: Procedure
Production comparing methanol and ethanol
  Materials
    Canola oil produced with ethanol and methanol
    WCO from different sources produced with methanol
Procedure
  Produce biodiesel by transesterfication
  Wash biodiesel
  Dilute biodiesel with DCM for use in GC
  Run samples through the GC
Dilution of Biodiesel

## Slide 12: GC Results
Different oil sources can yield different biodiesel ester profiles.
Waste cooking oil and virgin canola produce similar components.
WCO and virgin canola oil produce different relative amounts of components.
Alcohols have direct influence on composition of biodiesel.
Chart: 
| C15:0 | C16:0 | C17:0 | C17:1 | C17:2 | C18:0 | C18:1 | C18:2 | C20:0 | C20:1
Zoo | 0.14761 | 0 | 0 | 0 | 0.082881 | 0.2942 | 0.47217 | 0.0031346 | 0.0024943
Canola ME | 0.10239 | 0 | 0 | 0 | 0.031577 | 0.56999 | 0.29068 | 0.0053632 | 0.013975
Canola EE | 0.029653 | 0.055981 | 0.0024835 | 0.35474 | 0.070911 | 0.01762 | 0.31554 | 0.16439 | 0.0050876 | 0.013256

## Slide 13: Future Work
Determine if any other substances will allow for less water to be used in the biodiesel production.
Investigate the kinetics of the acid pretreatment.
Explore the next generation of biodiesel feedstock.
Explore uses of glycerin byproduct of biodiesel for making soap.
Glycerin Soap

## Slide 14: Thank You To
Dr.Mingming Lu, Faculty Mentor
Qingshi Tu, Graduate Assistant
Ming Chai, Graduate Assistant
Andrea Burrows, Grant Coordinator
Dr.Anant Kukreti, Principle Investigator