## Slide 1: Catalytic Electrode Coatings for Removal of Pesticides from Drinking Water in Ozonation/Electrolysis Treatment Systems RET Group Presentation July 30th, 2015 Ashley Gregory, 7th Grade Science, Gray Middle School Travis Hartberger, Chemistry & AP Chemistry, McKinley Tech High School
RET is funded by the National Science Foundation
grant # EEC-1404766.

## Slide 2: Project Outline
Topic Slides
Abstract 2
Background 3-6
Literature Review 7-10
Goals/Objectives 11
Tasks/Timeline 12
Training 13-15
Findings/Summary 16-22
Unit Plans 23-26
Bibliography 27-29
Acknowledgements 30

## Slide 3: Abstract
Abstract
2
This work details the assessment of catalysis on the synergistic ozonation/electrolysis degradation of atrazine
Atrazine degradation was optimal at a current density of 10.0mA/cm2
Manganese dioxide was evaluated as a heterogeneous catalyst on graphite by redox deposition and electrochemical deposition
The application of MnO2 as a suspended solid and as an anode and cathode, demonstrated limited to no improvement to the adsorption of and, subsequent, oxidation of atrazine by ozone

## Slide 4: Why We Are Concerned
USGS modeling results predict Atrazine levels of concern in surface water nationwide.
[1] Stone, W. W. and Bucknell, M. S., 2014, Watershed Regressions for Pesticides (WARP): U.S. Geological Survey Web Page, http://dx.doi.org/10.5066/F7R20ZD3
Closer to home
Introduction/
Background
3

## Slide 5: Closer to Home
A USGS study detected 42 pesticides and related compounds, including Atrazine, in the water in East Fork Lake, a water source for over 40,000 people.
modern campground
swimming beaches
picnic areas
horse riding trails
hiking and backpacking trails
mountain bike trails
Introduction/ Background
4

## Slide 6: Atrazine, Our Model Pesticide
Atrazine is one of the most commonly detected pesticides in the country.
It is slow to degrade in water, and often is adsorbed onto soil particles.
Atrazine has been shown to:
  Increase the risk of breast cancer in women[2]
  Disrupt hormones and act to “feminize” animals[2]
  Affect the human reproductive system[3]
[2] Roy, J.R.; Chakraborty, S.; Chakraborty, T.R. Estrogen-like endocrine disrupting chemicals affecting puberty in humans - A review. Medical Science Monitor 2009, 15, RA137-RA145.
[3] Agency for Toxic Substances and Disease Registry. Public Health Statement: Atrazine. 2003
Introduction/ Background
5

## Slide 7: Ozonation and Electrolysis
Ozone Quantitation
Detect aqueous ozone using the Indigo Method.5
Electrode
Optimization
Limited studies in electrode materials, i.e. MnO2 as a catalyst
Current Density
Quantity used to indicate the amount of current applied to a surface
Atrazine Degradation
reversed-phase high-performance liquid chromatography (HPLC).
Background
6
Why combine the two methods?[8]
combined
SYNERGY
ozone only
electrolysis
Notes: Citation for ozone quantification

## Slide 8: Catalytic Coatings
Catalyst – “a substance that increases the rate of a chemical reaction without itself undergoing any permanent chemical change.”
Change the properties of an electrode to provide various enhancements to the degradation of pollutants.
[4] Feng, Y. J., and Li, X.Y. (2003). "Electro-catalytic oxidation of phenol on several metal-oxide electrodes in aqueous solution." Water Research, Vol. 37 Issue 10, pp. 2399-2407.
Literature Review
7
Ti/RuO2
Ti/Sb-Sn-RuO2
Ti/Sb-Sn-RuO2-Gd
Pt
Ti-β-PbO2

## Slide 9: Catalytic Activity
Naydenov and Mehandjiev[5] reported a mechanism for MnO2’s (Z) role in mineralizing benzene.
Yang et. al.[6] showed mineralization Pharmaceutical Compounds (PhACs) with alumina-supported manganese oxide (MnOx) suspension
Literature Review
8
Mn2+
MnOx/CA
MnOx/CMA
MnOx/MA
Notes: CA = nonporous alumina
CMA = commercial mesoporous alumina
MA = synthetic mesoporous alumina

## Slide 10: Deposition of MnO2 (s)
Deposition Method
  Thermal deposition[4]
    Annealing Temperature[11]
  Electrochemical deposition
    Neutral pH[13] vs. Adjusted pH[14]
  Redox deposition[12]
Electrode substrate
  Molybdenum filling[16]
  Platinum priming[11]
  Graphite[12]
  Activated Carbon[15]
Literature Review
9
Fig. 4 SEM images of MnO2 (a) as prepared and dried at 50 °C in air (inset shows energy-dispersive X-ray spectrum) and annealed at (b) 200 °C, (c) 300 °C, (d) 400 °C, (e) 500 °C, and (f) 600 °C for 3 h in air. Arrows in (c) indicate initiation of nanorods.
50oC
200oC
300oC
400oC
500oC
600oC

## Slide 11: Current Density[7]
Since changes in current density will effect the voltage of the reactor, we want to explore the current density effects on the mechanism(s) for degrading atrazine
Similar studies show impact of current density on ozone generation
Literature Review
10
1.5kA/m2
1.0kA/m2
0.5kA/m2

## Slide 12: Goals/Objectives
Goal:
Optimize an ozonation/electrolytic treatment of drinking water for removal of pesticides (i.e. atrazine)
Objectives:
Evaluate the changes in current density (mA/cm2) on the mechanism of atrazine degradation
Evaluate the effectiveness of catalytically active electrodes on the degradation of atrazine
  1.) Anode: BDD & Cathode: SS
  2.) Anode: G & Cathode: SS
  3.) Anode: G w/ MnO2ED & Cathode: SS
  4.) Anode: G w/ MnO2RD & Cathode: SS
  5.) Anode: BDD & Cathode: SS (suspended MnO2)
  6.) Anode: BDD & Cathode: G w/ MnO2ED
  7.) Anode: BDD & Cathode: G w/ MnO2RD
  Note: BDD = Boron-doped Diamond TD = Thermal decomposition
  SS = Stainless Steel ED = Electrochemical deposition
  G = Graphite RD = Redox deposition
  Ti = Titanium
  MnO2 = Manganese dioxide (catalyst)
Goal/Objectives
11

## Slide 13: Tasks & Timeline
Research Tasks
Evaluate the effect of current density on the degradation of atrazine
Develop a catalytic coated electrode which can be applied to the atrazine degradation system
Characterize the system with the coated electrode
Timeline to Complete Research Tasks
Completed Tasks as of July 16, 2015
Evaluation of current density on atrazine
-10.0 mA/cm2 appears optimal
Completed Tasks as of July 20, 2015
1. Characterize the atrazine degradation system
  Testing different masses of MnO2 suspended within the atrazine solution
  Testing of developed catalytic electrodes in comparison to BDD electrode
Tasks & Timeline
12

## Slide 14: Training Received
Training Received
13
Figure 2: Graphite electrode coated with MnO2 (s) by anodic deposition using 0.25 M MnSO4*H2O (aq) with a current density of10mA/cm2 at 98oC and annealed at 450 oC
Figure 1: Anodic deposition of MnO2 (s) on graphite anode using a stainless steel cathode with 0.25 M MnSO4*H2O(aq) and a current density of 10mA/cm2.

## Slide 15: Training Received
Ozonation/Electrolysis Reaction Chamber:
Compressed oxygen cylinder
Ozone generator and flow meter
Potentiostat and electrode system
Ag/AgCl Reference electrode
Reaction sampling for ozone quantification and HPLC
Training Received
14
Notes: Preparation of Potassium Indigotrisulfonate solution (200mg/L)
  100 mL volumetric flask
  μΩ water (solvent)
  pH=2 buffer (2.22 mL H3PO4 & 5.62 g NaH2PO4)

## Slide 16: Training Received
Ozone Quantification[5]:
Preparation of Potassium Indigo
trisulfonate solution (200mg/L)
Absorbance using UV-Vis Spectrophotometer at 600 nm
Calibration: algebraic calculation of [ozone] in mg/L from absorbance
Degradation of Atrazine:
Preparation of HPLC vials using Na2S2O3 as an ozone quencher
Data collection from HPLC chromatograms (integration for area under the curve)
Training Received
15
Notes: Preparation of Potassium Indigotrisulfonate solution (200mg/L)
  100 mL volumetric flask
  μΩ water (solvent)
  pH=2 buffer (2.22 mL H3PO4 & 5.62 g NaH2PO4)

## Slide 17: Figure 1
The Effect of Current Density on Degradation of Atrazine
Findings
16
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport
1mA/cm2
10mA/cm2
38mA/cm2

## Slide 18: Figure 2
The Effect of MnO2 on Degradation of Atrazine
Findings
17
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
G/SS
G-MnO2/SS
BDD/SS
MnO2
reaction rate

## Slide 19: Figure 3
Cyclic Voltammetry
Findings
18
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
G-MnO2/SS
G/SS
BDD/SS
>1.4V
OER
>1.4V
OER

## Slide 20: Figure 4
The Effect of Current Density & Voltage on Degradation of Atrazine
Chart: Time (minutes)
6 minutes
4 minutes
2 minutes
0 minutes
Progress
19
electrolyte
atrazine
desethyl
desisopropyl
atrazine
desethyl
atrazine
desisopropyl atrazine
>20mA/cm2 exceeds mass-transport.
Chromatogram of Ozonation/Electrolysis (10mA/cm2)

## Slide 21: Figure 5
Reaction Pathway
Findings
20
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
O3 / OH
O3 / OH
O3 / OH
O3 / OH
OH
OH
[CO2, H2O, N2, Cl2]
OH
O3 / OH
OH
atrazine
DEA
DIA
DDA
cyanuric
acid
cyanuric
acid

## Slide 22: Figure 6
HPLC chromatograms at sampling times with ~90% atrazine degradation
Findings
21
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
>20mA/cm2 exceeds mass-transport.
Electrolysis
Atrazine is mineralized
Ozonation
Ozonation/Electrolysis
Ozone/Electrolysis + MnO2
MnO2
does not alter the pathway of atrazine degradation
Ozonation & ozonation/electrolysis combined are not significantly different

## Slide 23: Summary
Summary
22
Atrazine degradation was optimal at a current density of 10.0mA/cm2
At current densities >20.0mA/cm2, the ozonation/electrolysis synergism was less favored due to ozone stripping and current-limiting mass-transport.
The application of MnO2 as a suspended solid and as an anode and cathode, demonstrated limited to no improvement to the adsorption of and, subsequent, oxidation of atrazine by ozone
Manganese dioxide’s oxidant competition with ozone and no apparent change or improvement to the ozonation/electrolysis pathway to oxidize atrazine.

## Slide 24: Unit Topic: Using Green Infrastructures To Reduce Run-off Pollutants
Unit Plan
23
Development of Ballyshannon Way in Union, Kentucky
(Google Maps)
Course: Physical Science
Grade Level: 7
Essential Question: How can we decrease the amount of polluted run-off entering the surface water system in a developing community?
Challenge: To create a green infrastructure which will decrease the amount of pollutants entering the surface water system in a developing community.

## Slide 25: Unit Topic: Using Green Infrastructures To Reduce Run-off Pollutants
Unit Plan
24
General Outline of Unit Lessons and Activities:
Lesson One: Surface Water Pollution
Activity One: The Hook: Building A Water Filter
Activity Two: Natural and Urban Water Cycles
Lesson Two: Green Infrastructures
Activity One: Plant Roles in Green Infrastructures
Activity Two: The Challenge: Designing a Green Infrastructure

## Slide 26: Unit Topic: Creating a High Performance, “Green” Battery
Unit Plan
25
[17] Furlan, P.Y., Krupa, T., Naqiv, H., and Anderson, K. (2013). “An Open-Ended Project: Building a High Performance, yet Simple, Household Battery” Journal of Chemical Education. Vol. 90, 1341-1345.
Course: AP Chemistry
Grade Level: 11-12
Essential Question: How can we optimize use and type of household materials as well as electrode properties (surface area and spacing) to create a high-performance, “green” battery assembly?
Challenge: To build a high-performance, “green” battery assembly using common household materials that will be able to power the motors of various toy cars.

## Slide 27: Unit Topic: Creating a High Performance, “Green” Battery
Unit Plan
26
General Outline of Unit Lessons and Activities:
Lesson One: Intro to Electro chemistry
Activity One: The Hook: Building a standard battery-power car
Activity Two: Electrochemical and Electrolytic Cells
Lesson Two: Designing and Testing Batteries
Activity Three: Manipulating Components of a Battery
Activity Four: The Challenge: Designing a “Green” High-Performance Battery

## Slide 28: References
Stone, W. W. and Bucknell, M. S. (2014), “Watershed Regressions for Pesticides (WARP).” U.S. Geological Survey, http://cida.usgs.gov/warp/home/ (June 26, 2015)
Roy, J.R.; Chakraborty, S.; Chakraborty, T.R. (2009). “Estrogen-like endocrine disrupting chemicals affecting puberty in humans - A review.” Medical Science Monitor, Vol. 15, pp. RA137-RA145.
Agency for Toxic Substances and Disease Registry (2003). Public Health Statement: Atrazine CAS#: 1912-24-9.
Feng, Y. J., and Xiao Y. Li. (2003). "Electro-catalytic oxidation of phenol on several metal-oxide electrodes in aqueous solution." Water Research, Vol. 37, Issue. 10, pp. 2399-2407.
Naydenov, A. and Mehandjiev, D. (2003) Complete oxidation of benzene on manganese dioxide by ozone. Applied Catalysis A: General, 97 (1), 17-22.
Yang, L.; Hu, C.; Nie, Y.; Qu, J. (2009) Catalytic ozonation of selected pharmaceuticals over mesoporous alumina-supported manganese oxide. Environ. Sci. Technol., 43 (7), 2525-2529.
Bibliography
27

## Slide 29: References
Bader, H. and Hoigné, J. (1981). “Determination of Ozone in Water by the Indigo Method,” Water Research, Vol. 15, pp. 449-456
Kanani, N. (2005). Electroplating: Basic Principles, Processes and Practice. Elsevier, Ltd.
Vera, Y.M., José de Carvalho, R., Torem, M. L., Calfa, B.A. (2009). “Atrazine degradation by in situ electrochemically generated ozone” Chemical Engineering Journal, Vol. 155, pp. 691–697.
Qiua, C., Yuana, S., Li, X., Wanga, H., Bakheet, B., Komarneni, S., Wang, Y. (2014). “Investigation of the synergistic effects for p-nitrophenol mineralization by a combined process of ozonation and electrolysis using a boron-doped diamond anode,” Journal of Hazardous Materials Vol. 280, pp. 644–653
Wei, W., Xinwei Cui, X., Chen, W., and Douglas G. Ivey, D.G. (2011). “Manganese oxide-based materials as electrochemical supercapacitor electrodes,” Chem. Soc. Rev., Vol. 40, pp. 1697-1721.
Wua, M., Snooka, G.A., Chena, G.Z., Fraya, D.J. (2004). “Redox deposition of manganese oxide on graphite for supercapacitors,” Electrochemistry Communications, Vol. 6, Issue 5, pp. 499–504
Bibliography
28

## Slide 30: References
Shinomiyaa, T., Guptaa, V., Miura, N., (2006). “Effects of electrochemical-deposition method and microstructure on the capacitive characteristics of nano-sized manganese oxide,” Electrochimica Acta, Vol. 51, Issue 21, pp. 4412–4419
Hu, C. and Tsou, T. (2001). “Ideal capacitive behavior of hydrous manganese oxide prepared by anodic deposition,” Electrochemistry Communications, Vol. 4, Issue 2, pp. 105–109
Wang, J., Chen, Y., and Chen, B. (2015). “A Synthesis Method of MnO2/Activated Carbon Composite for Electrochemical Supercapacitors,” Journal of the Electrochemical Society, Vol. 162, Issue 8, pp. A1654-A1661
Nakayama, M., Tanaka, A., Sato, Y., Tonosaki, T., and Ogura, K. (2005) “Electrodeposition of Manganese and Molybdenum Mixed Oxide Thin Films and Their Charge Storage Properties” Langmuir, Vol. 21, pp. 5907-5913
Furlan, P.Y., Krupa, T., Naqiv, H., and Anderson, K. (2013). “An Open-Ended Project: Building a High Performance, yet Simple, Household Battery” Journal of Chemical Education. Vol. 90, 1341-1345.
Bibliography
29

## Slide 31
The RET program funded by the National Science Foundation
Grant ID# EEC-1404766
Project Faculty Mentor, Dr. Margaret Kupferle
Graduate Research Assistant, Mr. Greg Saylor
Project Faculty Mentor, Dr. George Sorial
RET Project Director and Principal Investigator, Dr. Anant R. Kukreti
Resource Person & Grant Coordinator, Debbie Liberi
RET Resource Teacher, David Macmorine
Acknowledgements
30