## Slide 1
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Modeling of Signalized Intersection Design and Impacts
Presented by
Lynn Brant
Kings High School
Girija Nair-Hart, PhD.
University of Cincinnati Clermont
2019 Summer NSF RET Project #4

## Slide 2
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Background
Goal
Research Activities
Understanding of Basic Concepts
Training Received
Case Study
Result Analysis
Class Implementation Plans
Outline of Presentation

## Slide 3
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Faculty Mentor
Mr. Raja Bharat Annam Graduate Research Assistant
U.C. MS Student in Transportation Engineering
Graduate Research Assistant
Heng Wei, Ph.D., P.E. Professor and Director Advanced Research on Transportation Engineering and Systems (ART-EngineS) Laboratory
Our Research Team

## Slide 4
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Problem Identification: complex of current signalized
intersections -- example of MLK & Jefferson
Big Idea: apply advanced signal control technology
Challenge: understand and create simulation-based practical solution and required analytics
4
Research Background

## Slide 5
RET is funded by the National Science Foundation,
Grant # EEC-1710826
To investigate the simulation-based method for evaluating the proposed solution to the complex signalized intersection through a case study of the “complex intersection” of Martin Luther King Drive, Jefferson Avenue, Vine Street, and Short Vine Street.
Research Goal
4

## Slide 6
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Evaluated existing condition of the studied “complex intersection”.
Proposed solution alternative aiming to improve the operational performance by using delay and level of service.
  Signal phase and timing improvement alternatives
  Roundabout alternative.
Used Simulation Software to evaluate the proposed alternatives.
Develop class implementation plans
6
Research Activities

## Slide 7
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Understanding of Basic Concepts
Types of Traffic Signals
Pre-timed
Semi – Actuated
Fully – Actuated
NEMA Phasing Convention

## Slide 8
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Mathematical Model for Actual Saturation Flow
Understanding of
Basic Concepts

## Slide 9
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Level of Service (LOS)
(Step function)
Performance Measures
Average Delay
Travel Speed
Level of Service
(LOS)
Understanding of
Basic Concepts

## Slide 10
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Understanding of Basic Concepts
LOS Interpretation
10

## Slide 11
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Software Training Learned from the Project
Highway Capacity Software
Micro-simulation VISSIM 9.0

## Slide 12
RET is funded by the National Science Foundation,
Grant # EEC-1710826
HCS – Highway Capacity Software
Geometric
Area type
Land details
Grade
Traffic
# vehicles
Base saturation flow rate
% heavy vehicle
Signalization
Cycle length
Green time etc
Type of intersection
Software Training

## Slide 13
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Vissim Interface
Base Data
(all imperial)
Background Setting
(google map zoom,
saved files)
Insert Links
(splines, connectors)
Create turn lanes
(map out the entire
∩)
Add Vehicle Input
Set Route Decisions
Identify Conflict
Areas
Add Signal Control
Ring Barrier Control
(RBC)
Signal Head
Detectors, Detectors to RBC
Software Training

## Slide 14
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Software Training

## Slide 15
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Software Training

## Slide 16
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Software Training

## Slide 17: Case Study Data for Simulation-based Analysis
RET is funded by the National Science Foundation,
Grant # EEC-1710826

## Slide 18
RET is funded by the National Science Foundation,
Grant # EEC-1710826
MLK - EPA
Case Study
VISSIM Simulation
MLK - Jefferson
  Vine Left Turn
MLK - Short Vine

## Slide 19: Case Study Simulated LOS using VISSIM
RET is funded by the National Science Foundation,
Grant # EEC-1710826
MLK Priority as Major Road

## Slide 20
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Seven Simulation Run Changes
Proposed Alternatives: Signal Changes

## Slide 21
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Cycle Length Changes
Proposed Alternatives:
Signal Changes

## Slide 22
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Fully Actuated Signal
VISSIM Simulation of the Proposed Alternatives

## Slide 23: Analysis of Simulation Results
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Data Analysis Components

## Slide 24: Analysis of Simulation Results
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Vehicle Delay Data
Cars (10) – 98%
of traffic flow
MLK
43.58
40.89
70.01
44.48
39.60
37.80
51.75
37.71
0.00
10.00 20.00 30.00 40.00 50.00 60.00
Average Delay in seoncds/vehicle
70.00 8
0.00
Current
Roundabout Signal Change 2
Signal Change 1-3
Signal Change 1-2
Signal Change 1-1
Pre-Timed Fully Actuated
Signal Changes
Vehicle Delay (10) on MLK EB Through Traffic
37.01
37.27
30.00 40.00
58.78
38.80
36.59
36.14
55.69
Roundabout 31.85 Signal Change 2
0.00
10.00 20.00
50.00 60.00
70.00
Signal Change 1-3
Signal Change 1-2
Signal Change 1-1
Pre-Timed Fully Actuated
Current
Average Delay in seconds/value
Signal Changes
Vehicle Delay (10) on MLK WB Through Traffic

## Slide 25
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Emissions Data
Analysis of Simulation Results
3782.27
3750.00 3800.00 3850.00 3900.00
Total Sum of Emission VOC in grams through all intersections
3831.25
3915.74
3843.19
3839.93
3787.78
3700.00
3950.00
Current
Fully Actuated
Pre-Timed
Signal Change 1-1
Signal Change 1-2
Signal Change 1-3
Signal Changes
Sum of Volatile Organic Compounds by Simulation Run
Emission Measures
Nitrogen Oxide
Carbon
Fuel
Consumption
Compounds

## Slide 26
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Challenge Visualizing Links & Connectors
Three Lane Roundabout Simulation
Proposed Roundabout
Vine St

## Slide 27
RET is funded by the National Science Foundation,
Grant # EEC-1710826
No Left Turns
Continuous Right Turn from MLK to Vine
Proposed Roundabout
Vine St

## Slide 28
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Final Recommendation
Delay
Reductions:
MLK EB – 13.3%
MLK WB – 1.8%
Simulation Signal Change 1 - 3

## Slide 29
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Limitations to Roundabout Simulation
Roundabout is most efficient under the condition of less than 600 vehicles/hour/lane
  Simulation vs. Real-life
    Extended Research before putting into
practice
      Non-intuitive Emission Data
Roundabout or Not?

## Slide 30
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Efforts of Traffic Engineers
29%
22%
28%
6%
9%
5%
2017 U.S. GHG EMISSIONS BY SECTOR
Transportation Agriculture
Electricity Commercial
Industry Residential
Never Look at Traffic Signal the Same Again
Many Factors

## Slide 31: Class Implementation Plan: Lynn’s Geometry Class
RET is funded by the National Science Foundation,
Grant # EEC-1710826
The Big Idea
CIRCLES used in TRANSPORTING
Revolving Doors for People
Roundabouts for Cars

## Slide 32
RET is funded by the National Science Foundation,
Grant # EEC-1710826
The Hook
Essential Question
- Model an efficient revolving door for the new entrance to King HS
Class Implementation Plan: Lynn’s Geometry Class

## Slide 33
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Challenge
  Build a scale model of a revolving door
  Efficiently move KHS students
  3-minute Sale Pitch
The Challenge
Class Implementation Plan:
Lynn’s Geometry Class

## Slide 34
Optimizing the Energy Expended by Heart Muscles during Blood Trafficking at the Intersection of
Artery, Capillary, and Veins
Classroom Application The Calculus Process of
Optimization
Research Optimizing traffic flow at
the intersections
C F D
Vissim 9.0
Class Implementation Plan:
Girija’s Calculus I Class
Benefits Application – real life connection- hands-on

## Slide 35
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Acknowledgement
Dr. Heng Wei, Faculty Mentor
Mrs. Lora Buchanan, RET Program Coordinator Dr. Margaret Kupferle, RET Principal Investigator
Mrs. Pamela Truesdell, Instructor, Engineering Design Course
Mr. Raja Bharat Annam, Graduate Research Assistant Dr. Qingyi Ai, Industry Partner, Arcadis-US, Inc.
National Science Foundation
University of Cincinnati

## Slide 36
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Heart blood flow YouTube video
Highway Capacity Manual 2016
Manual on Uniform Traffic Control Devices 2009
Smithsonian Magazine
Traffic Signal Timing Manual
Vissim First-steps Manual
References

## Slide 37
RET is funded by the National Science Foundation,
Grant # EEC-1710826
Thank you for attending today!
37